## Slide 1: Recommended Revisions to Oregon’s Human Health Criteria for Arsenic
Presentation to the EQC
April 21, 2011
Debra Sturdevant, Jennifer Wigal, Neil Mullane
Notes: Chair Blosser, Commissioners, my name is Debra Sturdevant.
  We are here today to recommend that you adopt amendments to the water quality standards rule for toxic pollutants to revise the human health criteria for arsenic and to adopt an arsenic reduction policy.
I would like to first refresh your memory on some background and then provide an overview of the recommended rule changes and how DEQ derived the proposed criteria.

## Slide 2
Background:
2008 EQC directives:
  Cost effective and environmentally meaningful implementation of human health criteria
  Review the science for naturally-occurring earth metals (in response to testimony)
Embarked on metals review, working with Toxics Rulemaking Workgroup
Accelerated the review at request of stakeholders
Iron and manganese criteria revised Dec. 2010
Notes: In October 2008 the Commission directed DEQ to conduct rulemaking to revise Oregon’s human health criteria based on an increased fish consumption rate.
At that meeting, the Commission also directed DEQ to provide for cost effective and environmentally meaningful implementation of the human health criteria and to review the science behind the criteria for naturally occurring earth metals.
This last directive responded to public testimony that:
the current arsenic criteria are well below natural levels and
well below the drinking water standard for arsenic, know as the maximum contaminant level, established under the federal Safe Drinking Water Act.
DEQ embarked on a review of 3 metals, iron, manganese and arsenic, working with the stakeholder workgroup.
During the process, stakeholders requested that DEQ adopt the metals criteria revisions on an accelerated timeline, ahead of the larger human health criteria rulemaking, as the revisions would affect upcoming permit renewals and 303d listings .
    [20 segments listed for arsenic on the 2004/05 303d list]
The Commission adopted revisions to the iron and manganese criteria in Dec. 2010. However, DEQ decided to do additional work in response to public comment on the arsenic criteria, which we are proposing for adoption today.

## Slide 3
Policy Objective
Protect human health
Account for the presence of arsenic in Oregon waters from natural sources
Alternatives Considered
Current criteria (0.0022 µg/l)
Maximum contaminant level (10 µg/l)
Natural conditions based criteria
EPA calculation method adjusted for Oregon
Notes: For arsenic, the policy objectives for the new standard are… (from slide)
  [Criteria below commonly found natural background levels can lead to multiple 303d listings and TMDL studies for substances that can not be controlled. In addition, sources may be required to obtain variances to discharge substances naturally in their water supply. Where this occurs, state and discharger expenditures to address criteria exceedences will not result in environmental improvement or health benefits. ]
DEQ considered several alternatives:
For reference, the current criterion are 2 to 3 orders of magnitude lower than commonly found natural levels in Oregon waters.
Many states have simply adopted the MCL of 10 µg/l as their criterion; but 10 is much higher than natural levels in many Oregon waters and would allow human sources to increase arsenic concentrations to levels of concern.
  [The water quality standards in stream are intended to protect human health from exposure through both drinking water and eating fish.]
We considered basing criteria on natural conditions,
  vary; DEQ does not have sufficient data to set water body or regional criteria throughout the state, particularly for inorganic arsenic.
  In addition, natural conditions are not inherently protective of human health.
DEQ concluded, and the workgroup agreed, that the most scientifically defensible alternative is to use EPA’s calculation method, but to adjust some of the factors to be more appropriate for Oregon. Therefore, we looked into the factors that could vary based on local data or state policy choices.

## Slide 4
Human Health Criteria for Arsenic (µg/l) |  |  | 
 | Water + Fish Ingestion | Fish Consumption Only - Freshwater | Fish Consumption Only - Saltwater
Current criteria (total arsenic) | 0.0022 | 0.0175 a | 0.0175a
Criteria proposed Aug 2010 (inorganic arsenic) | 2.3 | 2.7a | 2.7a
Recommended criteria (inorganic arsenic) | 2.1 | 2.1 | 1.0
a Current and initially proposed ‘fish consumption only’ criteria applied to all waters.
Notes: To jump to the bottom line, shown on this table in orange, the criteria DEQ is recommending are 2.1 for both the water and fish ingestion and the fish consumption only criteria for freshwater; and a separate saltwater fish consumption criterion of 1.0 µg/l.
This table also shows the criteria we initially proposed for public comment and the current criteria for reference.
Next, I would like to discuss some of the major areas of public comment we heard and then go through how we derived the recommended criteria in more detail.
  [There is a limited data set now, but it should improve with more toxics monitoring and measurement of inorganic arsenic; also because the quantitation limit (for total As) has been lowered from 5 to 0.5 µg/l.)]

## Slide 5
Areas of Public Comment
Fish consumption rate of 175 g/d
  Recommend that DEQ withhold submittal to EPA until the Commission acts on the human health criteria
Waters with higher natural arsenic levels
  Evidence of this in the Klamath and Malheur basins
  DEQ will consider site specific criteria and/or use changes
  Priority to revise statewide criteria in timely manner
Do a better review of the science
  Particularly for bioconcentration
  Don’t rely on method used by other states
Notes: Fish consumption rate
One area of public comment was the increased fish consumption rate.
In order to ensure consistency in the consumption rate used for all criteria, DEQ proposes to withhold submitting the arsenic criteria to EPA until after the EQC acts on the human health criteria rulemaking. The new arsenic criteria would not be applicable until after EPA approval.
Waters with high Natural Arsenic
Some water bodies have natural arsenic levels higher than the proposed criteria. For example, evidence of this in the Klamath and Snake River basins was provided by commenters.
DEQ’s current priority is to revise the statewide criteria in a timely manner. However, we agree that it may be appropriate to establish site specific criteria for these water bodies.
  [May need to remove domestic water supply as use or issue variance.
  SSC based on: natural conc., alternate risk level, site specific BCF or IF.]
Better Science
DEQ received comment that caused us to look into the literature on bioconcentration and arsenic in the marine environment and to revise our proposed criteria based on the additional research.

## Slide 6
Criteria Calculation for Water and Fish Ingestion
Criterion (µg/l) = RF × BW
CSF [DW + (BCF × IF× FCR)]
RF = risk level factor BW = body weight
BCF = bioconcentration factor DW = drinking water intake
IF = inorganic proportion factor CSF = cancer slope factor
FCR = fish consumption rate
Notes: This slide illustrates the equation used to calculate human health criteria for cancer-causing pollutants.
In deriving Oregon specific arsenic criteria, DEQ adjusted factors that can vary geographically or for which the state has a policy choice. These factors include the risk level, the bioconcentration factor, the inorganic portion and the fish consumption rate.
We did not revise body weight, drinking water intake, or the cancer slope factor, which represents the toxicity of the pollutant and is published by EPA.

## Slide 7
Freshwater Criteria
Fish consumption rate = 175 grams/day
Bioconcentration factor = 14
  bioconcentration - amount of the pollutant in fish tissue compared to the concentration in the water
  Revised BCF for current criteria based on additional data
Inorganic portion = 10%
  the criteria are for inorganic arsenic, the toxic form
  a small portion of the arsenic in fish tissue is inorganic
Notes: This slide shows the values DEQ used to derive the freshwater criteria for arsenic. As discussed earlier, we used a fish consumption rate of 175 g/d.
Bioconcentration represents the amount of the substance in the water that accumulates in fish tissue.
  In calculating the proposed criteria, DEQ used a BCF of 14
  This value is the geometric mean of values from 4 studies:
    3 for trout and 1 for bluegill
  EPA’s BCF of 44, derived in the 1980s, is based on 2 values, 1 for bluegill and 1 for eastern oysters.
  The BCF of 14 uses the original 2 values, but also incorporates more recent data.
The inorganic portion adjusts for the fact that:
  BCF studies measured total arsenic, but the criteria are for inorganic arsenic.
  It is a form of inorganic arsenic that is known to be toxic
    [arsenite; As III]
  Inorganic portion = 10%
  Columbia basin and Willamette river fish tissue studies show a small portion of the arsenic in fish tissue is inorganic
    [All fish 10%; anadromous fish 1%]

## Slide 8
Freshwater criteria - Cancer risk level
Policy objective – avoid setting arsenic criteria below common natural background levels (up to 3 µg/l)
Because arsenic is naturally occurring, higher risk level is acceptable (generally use 10-6)
 | Risk Level | Criterion
Water and fish ingestion | 1 × 10-4 | 2.1 µg/l
Fish consumption only | 1.1 × 10-5 | 2.1 µg/l
Notes: In order to meet the policy objectives to protect human health and avoid setting criteria below common natural levels, DEQ used a risk level of 10-4 for the water and fish ingestion criterion; and a risk level slightly above 10-5 for the fish consumption only criterion.
Cancer risk is a factor where the state has a policy choice. Typically, Oregon bases our criteria on a risk level of 1 in one million or 1x10-6.
EPA guidance allows states to use risk levels of 10-5 for the general population,
and 10-4 when paired with consumption rates based on regular or subsistence consumers, as our proposed rate is.
Where arsenic is natural, the risk is not new or human caused; it has been present since people have been eating fish and drinking from Oregon waters.
  [At exactly 1x10-5, the criterion would be 1.9 µgl. It would not make sense for the criterion for one path of exposure (fish consumption) to be more stringent than the criterion based on two paths of exposure (fish and water). Therefore, DEQ recommends that the criteria be the same.]
Because the ‘fish and water’ criterion is based on the higher risk level, DEQ recommends that the EQC adopt an “Arsenic reduction policy” to ensure that risk is minimized where possible in drinking water. I will discuss this further in a moment.

## Slide 9
Evaluation of Saltwater Arsenic Criteria (total inorganic) |  |  | 
Fish consumption | 175 g/d | 175 g/d | 
Bioconcentration | 26 | 350 | 
Inorganic portion | 10% | 1% | 
Risk level | 1 × 10-5 | 1 × 10-5 | 
Natural ocean level |  |  | 1 – 1.2 µg/l
Criterion | 1.0 µg/l | 0.8 µg/l | 1.0 µg/l
Notes: DEQ is proposing a separate fish consumption only criterion for saltwater of 1.0 µ/l.
Due to the limited bioconcentration data and the complexities of arsenic in the marine environment, DEQ evaluated the saltwater criteria 3 ways. First, we looked at 2 calculations scenarios, both using a fish consumption rate of 175 grams/day.
The first scenario (shown in the first column) uses the same data as the freshwater criterion except that it incorporates data for oysters, bringing the bioconcentration factor up from 14 to 26.
  There are no saltwater fish or vertebrate bioconcentration data; the only saltwater data is for oysters, which are invertebrates. This approach assumes that marine finfish will respond similarly to freshwater finfish in their arsenic intake. In the absence of better data, it is one reasonable approach. [oyster bcf = 350]
The second scenario uses only the oyster value of 350 for bioconcentration, and the resultant criterion is slightly lower.
  Did this second calculation because the literature suggests that bioconcentration of total arsenic may be higher in the marine environment.
  The literature also indicates, however, that less of the arsenic in fish tissue is inorganic, particularly arsenite (As III), which is the toxic form.
  Inorganic 1% based on tissue data for saltwater species
      A criterion of 1.0 represents a risk level of 1.3 x 10-5.
3. Last, we looked at data on natural ocean levels:
Well accepted that ocean levels for total arsenic are 1-3 (1.7-2) µg/l.
Accepted that total inorganic is a large portion of that, but that arsenite is a smaller amount
Limited data on inorganic; average of 1.1 or 1.2 total inorganic in Pacific ocean (Tanaka)

## Slide 10
Arsenic Reduction Policy
Purpose: Minimize health risk from human sources of arsenic where the water arsenic concentration is below the criteria
Targets: Industrial discharges to drinking water source water protection areas
  If the source has the potential to increase the arsenic concentration in the source water
Requires: Arsenic reduction plan
Notes: ARP recommended because water and fish criterion based on 10-4 risk level.
Go over the slide.
The rule includes a procedure to assess whether a source has the potential to impact a drinking water source, which will be further detailed in an implementation document.
Arsenic reduction plan: feasible pollutant reduction measures, implementation schedule, monitoring and reporting requirements.
[Does not include municipal dischargers because they requirements to monitor and develop pollutant reduction plans under SB 737. These plans are required when muni discharges greater than 10µg total arsenic; ARP considers potential to increase stream concentration of inorganic arsenic; so not exactly the same, but both require pollutant reduction plans for significant sources. 737 plans not limited to drinking water source water protection areas.]

## Slide 11
DEQ recommends that the EQC adopt the amendments to the toxics water quality standard rule shown in attachments A and B:
  Revised numeric arsenic criteria
  An arsenic reduction policy
  Revisions not applicable until approved by EPA
To ensure consistency in the consumption rate, DEQ will submit the revised arsenic criteria to EPA after the Commission acts on the upcoming toxics criteria revisions.
Notes: To summarize, …
Which means that these criteria revisions will not become effective until we
The toxics water quality standards rule amendment scheduled to come to the EQC at your next meeting in June.
Happy to answer any questions.