## Slide 1: Envisioned Use of the Implementation Tools to Address Background Concentration
Introduction and summary of issue
Use of demographics to help define tools
Step-wise approach based on level of water quality protection
  Intake credits
  General permits +intake credits
  Background concentration allowance
  Variances
Departmental recommendations
Feedback / decision points
Next steps

## Slide 2: Introduction and Summary of Issue
Issue of “Background Pollutants” has been of major concern to all parties involved. Accordingly, a significant amount of RWG and Departmental effort has been focused on the development of implementation tools to help resolve this concern
  Industrial facilities were identified as being particularly susceptible to back ground pollutant permitting issues due to the many processes (intentional & unintentional) that tend to evaporate off water and concentration any background pollutants
  The Department has evaluated the following tools as being able to help resolve this issue:
    General Permits
    Multiple discharger variance for non-contact cooling water facilities
    Background pollutant allowance (De Minimus)
  In addition, individual variances may be on option and intake credits are available where there is not an increase in mass or concentration

## Slide 3: Use of demographics to help define tools
The Department looked at the demographics of the pool of ~149 individual industrial permits, looking to identify subclasses that would have particular concerns (increased concentration) and worked with permit writers and stakeholders to tailor appropriate responses
  The Department looked at:
    Industry type
    Pollutants of concern
    Discharge locations
    Size / flow rates
  Of particular concern were facilities that use surface or ground water for non-contact cooling that typically increases concentration from 2 to 8 times. ~39 facilities, 15 that discharge to a 303 d limited water bodies.

## Slide 4: Step wise approach based on level of water quality protection
First approach is to investigate use of an intake credit
  No increase in mass or concentration
  No environmental impact
  Second approach is to investigate the applicability of general permits for specific process activities such as non-contact cooling, boiler blow down or wash water.
Notes: Can also discuss how this is not limited to strictly “non-contact cooling water” and can be applicable to other activities. For example a large plant might have multiple general permits or in the future, a new type of general permit could be developed to handle multiple “utility water” funtions.
  This would require that the activity have an independent connection to outfall. General permits are designed to balance the water quality goals of preserving stream flow and the control of temperature and pollutants. Once the activity/s is/are addressed, the balance of the industrial process can then be re-evaluated using an intake credit.
  No increase in mass, insignificant increase in concentration
  Limited to Minor industrial facilities or activities. 12 of 15 non-contact facilities that discharge to 303 d limited waters.
  Environmental impacts are balanced to support overall water quality goals

## Slide 5: Cont.- Step wise approach based on level of water quality protection
  Third approach is to investigate the applicability of the background concentration allowance for any facilities that can not utilize the first two approaches and meet the qualifying requirements.
  This approach is designed for facilities that source their waters from water quality limited water bodies and their discharge is considered insignificant
  No increase in mass, insignificant increase in concentration
  Qualified by “No technologically or economically feasible means are available to reduce the pollutant concentration in the discharge that would not have other adverse environmental impacts.”
Notes:   Environmental impacts are balanced to support overall water quality goals

## Slide 6: Step wise approach based on level of water quality protection
  Final approach (as proposed) is to investigate the applicability of individual variances for any facility that can demonstrate meeting one of the six variance conditions set forth under 131.10 (g).
Notes:   This approach differs significantly from the first three in this approach requires a “Director and EPA approval” where the previous three can be facilitated through the permit development process and the regional permit writer. This approach is designed for facilities that source their waters from water quality limited water bodies and their discharge may have a significant affect of the in-stream concentration. This approach is considered an interim measure until a TMDL and waste load allocations can be developed.
  No increase in mass, potentially significant increase in concentration
  Qualified by requirements under 131.10 (g) and requires Director and EPA approval
  Environmental impacts are minimized (using pollutant minimization plans) until TMDL and Waste Load Allocations can be developed
  At this time the Department does not find a compelling justification to support the development of a multiple discharge variance

## Slide 7: Departmental Recommendations
  Approve and implement Intake Credit procedure
  Develop guidance describing the use of general permits in conjunction with individual permits no need for rule revision
  Approve and implement Background Concentration Allowance (De-Minimus) as a water quality standards rule
  Do not adopt multiple discharger variance for non-contact cooling facilities at this time (We’ll discuss this later during our presentation)

## Slide 8: Today’s Discussion
  Brief description of the three tools considered including short Q/A
  Group discussion of the Department’s recommendations
Follow group discussion we will have a poll on support on Departmental recommendation
Next Steps

## Slide 9: Next Steps for the Selected Implementation Tools
  If accepted, further develop Background Concentration Allowance.
  Develop guidance and calculation spreadsheets for Intake Credits
  Develop guidance for use of general permits in conjunctions with individual permits
  Continue discussion on individual variance language (May 20th meeting)