## Slide 1: Corrections and Clarifications to Toxics Water Quality Standards Rulemaking Public Hearing Portland Sept. 18, 2013
Andrea Matzke, DEQ

## Slide 2
To correct toxics criteria that were recently disapproved by EPA
  Focusing on the straight-forward corrections
To correct typos and errors from past toxics rulemakings and to propose additional clarifications
Why is DEQ Conducting This Rulemaking?
Notes: -Will briefly mention the other pollutants that were disapproved

## Slide 3
EPA Disapproval Actions:
  On Jan. 31, 2013, EPA disapproved criteria submitted by DEQ in 2004 associated with 11 pesticides and selenium, and noted errors with several footnotes
  Clean Water Act requires OR to fix the disapprovals or EPA is required to promulgate criteria for OR
Currently, DEQ has 3 effective toxics tables—confusing to public and DEQ staff
DEQ inadvertently omitted criteria for two pollutants during a 2007 rulemaking
There were a number of typos from past rulemakings and there are new DEQ table formatting recommendations
Why is DEQ Proposing to Make These Changes?
Notes: -After the State submits adopted rules, EPA must either approve (w/in 60 days) or disapprove (w/in 90 days). Disapproval must specify changes needed to assure compliance with requirements

## Slide 4
Concentrations of pollutant at which aquatic life, such as fish, shellfish and aquatic insects are protected
Each pollutant can have up to 4 criteria values:
  2 values to protect against acute and chronic effects in freshwater
  2 values to protect against acute and chronic effects in saltwater
A water quality standard is comprised of a beneficial use, criteria to protect the use, and antidegradation protections
What Are Aquatic Life Toxics Criteria?
Beneficial Use Protected: Fish and Aquatic Life

## Slide 5
Table 30 |  |  |  |  |  |  |  | 
Aquatic Life Water Quality Criteria for Toxic Pollutants |  |  |  |  |  |  |  | 
 | Pollutant | CAS No. |  | Human Health Criterion | Freshwater |  | Saltwater | 
 |  |  |  |  | (µg/L) |  | (µg/L) | 
 |  |  |  |  | Acute Criterion (CMC) | Chronic Criterion (CCC) | Acute Criterion (CMC) | Chronic Criterion (CCC)
33 | Pentachlorophenol |  | 87865 | y | See H | See H | 13 | 7.9
H Freshwater aquatic life values for pentachlorophenol are expressed as a function of pH, and are calculated as follows: CMC=(exp(1.005(pH)-4.869); CCC=exp(1.005(pH)-5.134). |  |  |  |  |  |  |  | 
34 | Phosphorus Elemental | 7723140 |  | n | -- | -- | -- | 0.1
35 | Polychlorinated Biphenyls (PCBs) | NA |  | y | 2 K | 0.014 K | 10 K | 0.03 K
K This criterion applies to total PCBs (e.g. determined as Aroclors or congeners) |  |  |  |  |  |  |  | 
36 | Selenium | 7782492 |  | y | See C , L | 4.6 C | 290 C | 71 C
C Criterion is expressed in terms of “dissolved” concentrations in the water column. |  |  |  |  |  |  |  | 
L The CMC=(1/[(f1/CMC1)+(f2/CMC2)]µg/L) * CF where f1 and f2 are the fractions of total selenium that are treated as selenite and selenate, respectively,and CMC1 and CMC2 are 185.9 μg/L and 12.82 μg/L, respectively. See expanded endnote F for the Conversion Factor (CF) for selenium. |  |  |  |  |  |  |  | 

## Slide 6
SUMMARY:
Corrections to toxics criteria to protect aquatic life
  11 pesticides
  Selenium
  Re-adopt arsenic and chromium criteria
Consolidate 3 aquatic life toxics criteria tables into 1 table (and delete references to the 3 tables in DEQ rules)
Additional miscellaneous corrections, clarifications, and formatting changes to toxics rule water quality standards regulations and associated criteria tables
What Rule Changes is DEQ Proposing to Make?
Notes: -Will provide more details later

## Slide 7
  Aquatic life criteria have the following frequency and duration components (in addition to magnitude/value):
  Duration:
    Acute (CMC)—1 hour average
    Chronic (CCC)—4 day average
    Frequency: Both acute and chronic values can’t be exceeded more than once every 3 years.
  Frequency and duration components of most of the pesticide criteria are different than the other aquatic pollutants
  Most of the pesticide criteria were developed prior to the 1985 EPA Guidelines and were developed with an alternate frequency and duration (i.e. acute can’t be exceeded any time and the chronic can’t be exceeded based on a 24 hr. average)
Correct Criteria for 11 Pesticides

## Slide 8
  Problem:
  DEQ correctly footnoted these pesticides, but by adding the general frequency and duration to the intro paragraph of the toxic tables, EPA determined that this addition effectively changed the frequency and duration of the pesticides despite the existing footnote.
  DEQ Proposes To:
Add clarifying language to the intro paragraph noting the pesticide frequency and duration exception
Revise the pesticide footnote to read more clearly
Correct Criteria for 11 Pesticides

## Slide 9
Problem:
DEQ did not apply the conversion factors to the freshwater criteria to convert a total recoverable result to a dissolved expression as intended in 2004
The dissolved form of metal is the more available or toxic form of a metal
  DEQ Proposes To:
  Apply the correct conversion factors
Correct Selenium Criteria

## Slide 10
  Problem:
  DEQ inadvertently omitted aquatic life criteria for arsenic and chromium VI from a toxics criteria table during a 2007 rulemaking.
  DEQ proposes to:
  Re-adopt freshwater and saltwater criteria for arsenic and saltwater criteria for Cr VI as originally proposed as part of the 2004 rulemaking
Re-adopt Arsenic and Chromium VI Criteria

## Slide 11
Problem:
Currently, there are 3 effective toxics tables—confusing to implement
DEQ Proposes To:
Delete Tables 20, 33A, 33B which contain the aquatic life criteria and replace with consolidated new Table 30
Delete references to Tables 20, 33A, and 33B in the Toxics Rule and in the Groundwater and Bacteria Rules, and instead reference aquatic life toxics criteria in the Toxics Rule (OAR 340-041-0033) instead of a specific table.
Consolidate Aquatic Life Toxics Tables

## Slide 12
Correct:
Reference typos in Arsenic Reduction Policy
Footnote typos and clarifications in aquatic life criteria tables
Table 40: Human Health Toxics
  typos
  clarified arsenic footnote
  corrected a criterion to two significant digits
  Table 33C: Aquatic Life Guidance Values for Toxics
  rename Table 33C to Table 31
  correct a reference in the intro language
  remove arsenic guidance values—regulatory aquatic life criteria already exist
Formatting in Tables 30, 31, and 40 to reflect current Agency guidelines
Other Corrections and Clarifications

## Slide 13
All proposed revisions to the Toxics Rule will become effective on April 18, 2014 (and after EPA approval)
Proposed revisions to the Bacteria and Groundwater Rules would become effective upon EQC adoption and filing with the Secretary of State.
When Will These Proposed Revisions Become Effective?

## Slide 14
Open for public comments: Sept. 1 – Sept. 30
Respond to public comments and revise as needed: Oct.
Present to the Environmental Quality Commission for adoption: Dec. 11-12
File with Secretary of State: Dec. 17
Submit to EPA for approval: Jan. 2014
Rulemaking Schedule

## Slide 15
DEQ Invites Your Comments!
Online: http://www.deq.state.or.us/regulations/proposedrules.htm
By mail: Oregon DEQ
Attn: Andrea Matzke
811 SW Sixth Ave.
Portland, OR 97204
By fax: 503-229-6037
Attn: Andrea Matzke
At today’s hearing: Submit written comments or testimony