## Slide 1
Overview
Rule clean-up
Update particulate matter (PM) standards
Categorically Insignificant Activities
Splitting businesses
New Source Review (NSR)
Extensions for NSR permits
Net air quality benefit for sensitive areas
Notes: Here is an overview of the topics we are going to cover today:
Rule clean-up
Update statewide grain loading and opacity standards
We have a defined term: Categorically Insignificant Activities
How emissions are divided when a business splits into two or more businesses
Our pre-construction program called New Source Review (NSR)
If construction is delayed, how a business an get an extensions for their NSR permit
Another defined term: Net air quality benefit
All of these topics will be explained in more detail later in this presentation.

## Slide 2: PM Standard – why change?
Add significant digit to standards consistent with EPA policy
  0.1 » 0.10
  0.2 » 0.20
Phase out 0.20 standard for older sources to help address newer/tighter ambient air quality standards (260 µg/m3 vs. 35 µg/m3)

## Slide 3: PM Grain Loading Standards Original Proposal
Source | Grain Loading Standards (gr/dscf) |  | 
 | Current Limit | Effective upon Rule Adoption | 2019
Built before 06/01/70 | 0.2 | 0.20 | 0.10
Built after 06/01/70 within 5 miles of “sensitive” area | 0.1 | 0.10 | 0.10
Built after 06/01/70 outside 5 miles of “sensitive” area | 0.1 | 0.1 | 0.10
Notes: This is an overview of the proposed changes to the grain loading standards.
“Sensitive areas” are designated because of air quality problems

## Slide 4: Proposed Opacity Rule Changes
Source | Opacity |  |  |  | 
 | Current Limit | Upon rule adoption | Exceptions | 2020 | Exceptions
Non-wood fired built before 06/01/70 outside special control area | 40% | 40% | NA | 20% | NA
Non-wood fired built before 06/01/70 inside special control area and built after 06/01/70 | 20% | 20% | NA | 20% | NA
Wood fired built before 06/01/70 | 40% | 40% | 55% for 12 minutes | 20% | 40%*
* - for 12 minutes
- during grate cleaning under plan
- boiler specific limit greater than 20% opacity, but not greater than 40% opacity, based on the opacity measured
during a source test that demonstrates compliance with grain loading

## Slide 5: Proposed Grain Loading Rule Changes for Non-Fuel Burning Equipment
Source | Grain Loading Standards (gr/dscf) |  |  | 
 | Current Limit | Upon Rule Adoption | Upon Rule Adoption | 2020
Built before 06/01/70* | 0.2 | 0.10 if data < 0.08 | 0.2 if data > 0.08 | 0.15
Built after 06/01/70 | 0.1 | 0.10 if data < 0.08 | 0.1 if data > 0.08 | 0.15
*Equipment or fuel used less than 876 hours/year limited to 0.20 gr/dscf

## Slide 6: Proposed Grain Loading Rule Changes for Fuel Burning Equipment
Source | Grain Loading Standards (gr/dscf) |  |  |  | 
 | Current Limit | Effective upon Rule Adoption | Effective upon Rule Adoption | 2020 | 2020
Built before 06/01/70* | 0.2 | 0.10 if data < 0.08 | 0.2 if data > 0.08 | 0.15 | 0.17**
Built after 06/01/70 | 0.1 | 0.10 if data < 0.08 | 0.1 if data > 0.08 | 0.15 | NA
*Equipment or fuel used less than 876 hours/year limited to 0.20 gr/dscf
** Source may request 0.17 gr/dscf if optimization doesn’t meet 0.15 gr/dscf

## Slide 7: Estimated Costs of Compliance with Particulate Matter Limits
 | Estimated Cost
Simple Boiler Tune-Up | $2,000 - $11,000
Extensive Boiler Tune-Up | $33,000 - $65,000
Multiclone Inspection | $3,000 - $4,000
Flue Gas Recirculation | $30,000 - $100,000
Multiclones | $60,000 - $100,000
Ceramic High Efficiency Multiclones | $110,000 - $120,000
Engineering Analysis for higher limit | $2,000 - $8,000
Continuous Opacity Monitoring System | $18,000 - $70,000