## Slide 1: New Source Review (NSR)
Proposing revisions to New Source Review program

## Slide 2: New Source Review (NSR)
Pre-construction permitting program mandated by Clean Air Act
  Maintain and protect air quality
  Requires pollution control devices where appropriate
Three distinct programs
  Prevention of Significant Deterioration (PSD) in attainment areas
  Nonattainment NSR
  Minor NSR
Major
NSR
}

## Slide 3: Things unique to DEQ’s program
Major source definition in nonattainment and maintenance areas
  Lower threshold than EPA definition
Offsets and Net Air Quality Benefit
  NAQB requires air dispersion modeling
  EPA program only requires offsets
  …

## Slide 4: Things unique to DEQ’s program, cont.
DEQ program requires air quality impact analysis for minor sources
Maintenance areas
  Former nonattainment areas
  DEQ program has more stringent requirements than federal program

## Slide 5: Why make changes?
Areas of the state are close to or are exceeding the PM2.5 National Ambient AQ Standards
  New PM2.5 standards adopted in 2007 – much lower than PM10 standards
  AQ problems mainly due to area sources, not industrial sources
Current rule structure
  does not adequately address PM2.5 ambient air quality problems
  prohibits development in small communities

## Slide 6: How will the changes improve the program?
New or modified sources can help address ambient air quality problems
Allows for development while improving or maintaining air quality

## Slide 7: What are the changes?
Align definition of major source with EPA’s definition
  Different requirements for small and large sources
Create 2 new area designations
  Help prevent nonattainment
  Eliminate permitting roadblock
  Get to maintenance faster
Primarily affect Minor New Source Review

## Slide 8: Major / Minor NSR – currently With construction or change in method of operation (Major Modification)
Emission Rate> Area designation, major mod? | 100*/250 tpy or more | SER to 99*/249 | Less than SER
Attainment | Major | Minor | n/a
Emission Rate> Area designation, major mod | SER or more | Less than SER
Nonattainment | Major | n/a
Maintenance | Major | n/a
  * Applies to 28 source categories listed in rule (e.g. pulp and paper mills, iron and steel mills, chemical process plants)

## Slide 9: Major / Minor NSR – proposed With construction or change in method of operation (Major Modification)
Emission Rate> Area designation, major mod? | 100*/250 tpy or more | SER to 99*/249 | Less than SER
Attainment | Major | Minor | n/a
Emission Rate> Area designation, major mod | 100 tpy or more | SER to 99 | Less than SER
Nonattainment | Major | Minor | n/a
Maintenance | Major | Minor | n/a
Overall stringency remains the same

## Slide 10: Significant Emission Rate (SER)
Pollutant | SER, tons per year
PM2.5 | 10
PM10 | 15
NOx, VOC, SO2 | 40
CO | 100
GHG | 75,000

## Slide 11: Two New Area Designations
Sustainment area
  Proposed rules designed to help keep area from becoming nonattainment
Reattainment area
  Proposed rules designed to be less stringent for smaller sources to encourage development, but still protect air quality

## Slide 12: Current Area Designations
Attainment
(AQ below NAAQS)
Nonattainment
(AQ at/over NAAQS)
Maintenance
(attainment)

## Slide 13: Areas in transition
Nonattainment
(AQ below NAAQS)
Attainment
(AQ at/over NAAQS)
Attainment
(AQ below NAAQS)
Nonattainment
(AQ at/over NAAQS)
Maintenance
(attainment)

## Slide 14: New Area Designations
Nonattainment
(AQ below NAAQS)
Attainment
(AQ at/over NAAQS)
Attainment
(AQ below NAAQS)
Nonattainment
(AQ at/over NAAQS)
Maintenance
(attainment)
Sustainment
Reattainment

## Slide 15: Changes to Improve Air Quality
“Priority sources” are primarily responsible for poor air quality (e.g. woodstoves in some communities)
Provide incentives for reducing priority source emissions
  More credit for emission reductions from priority sources
EQC can specify Priority Sources in sustain., nonattain., reattain. and maintenance areas

## Slide 16: Offset Changes
Major NSR, some ratios higher than current (1.2:1)
Minor NSR, ratios lower than major NSR
Ratios area-specific
Ratios reducible for priority source offsets
  E.g. 1.2:1  1:1
No changes to ozone offset requirements

## Slide 17: Net Air Quality Benefit Changes
Current NAQB criteria nearly impossible
Revise NAQB criteria
  Protect air quality:
    Focus on areas with worst air quality, and
    Prevent further degradation
  Reduce emphasis on industrial emission offsets/mitigation
  Eliminate problem with current criteria

## Slide 18: Last: Rule Organization
Minor New Source Review rules applicable to SER and over called State NSR program
  No change to other Minor NSR rules (e.g. permit requirements applicable to less than SER)
Division 224
{
Major NSR
State NSR
Offset requirements
Net Air Quality Benefit

## Slide 19: Summary of Proposed Changes
Raise Major source threshold to 100 tpy in nonattainment and maintenance areas
Create two new area designations: sustainment and reattainment
Indentify Priority Sources
Revise offset requirements
Revise Net Air Quality Benefit requirements
Major and State NSR in Division 224

## Slide 20: New Source Review (NSR)