## Slide 1: PERMITTING PROGRAM UPDATES
AKA Kitchen sink rules

## Slide 2: In a nutshell:
Move procedural requirements from definitions in Division 200
Division 200 before
Division 200 after

## Slide 3: Nutshell 2
Combine redundant definitions and move to Division 200
Clarify requirements for how to:
  Permit emergency generators
  Permit sources that want to be combined or split
  Grant extensions for NSR/PSD permits
  Determine compliance for all standards

## Slide 4: Nutshell 3:
Update Continuous Monitoring and Source Sampling Manuals (1992).
CMM
It’s about time!

## Slide 5: Repeal:
4-County Rules (Clackamas, Columbia, Multnomah, Washington)
Primary Aluminum
Sulfite Pulp Mill
Laterite Ore Production of Ferronickel
Charcoal Plant
Spray Paint

## Slide 6: NEW SOURCE REVIEW
Separate Major New Source Review from Minor New Source Review
Redefine Federal Major Source
  100 tpy in NAA, transitional or maintenance area
  Non-Federal Major = SER to 100 tpy

## Slide 7
Define “Transitional” Area:
  Nonattainment Area that has 3 years of “clean” data but not yet designated maintenance by EPA
Define “Potential Nonattainment” Areas
  Area that has monitored exceedances but not yet designated NAA by EPA or close to exceeding
New Source Review (cont.)

## Slide 8: New Source Review (cont.)
Source | Attainment | Potential NAA | NAA | Transitional | Maintenance
Federal Major | BACT Offsets Modeling | Preconstruction monitoring OR Can’t build | LAER Offsets (<1.2:1) | LAER Offsets (<1.2:1) | BACT Offsets (1.0:1) Modeling
Non-Federal Major | Modeling | Modeling OR Offsets (<1.0:1) | BACT Offsets (<1.0:1) | BACT Modeling OR Offsets (<1.0:1) | BACT Modeling OR Offsets (<1.0:1)

## Slide 9: New Source Review (cont.)
Redefine Net Air Quality Benefit for Federal Major Sources (sorry Pat H! )
  Require 1.2:1 offsets or
  Reduce to 1.0:1 offsets by offsetting emissions from “priority” sources:
    Woodstoves
    Sources causing NAA problem
  Modeling for PSD Class II Increments

## Slide 10: New Source Review (cont.)
Give non-federal major sources more flexibility
  Modeling OR
  Allow < 1.0:1 offsets
    Reduce to 0.5:1 offsets by offsetting emissions from “priority” sources:
      Woodstoves
      Sources causing NAA problem

## Slide 11: Last but not least……
Tighten grain loading and opacity standards for older sources that were built before June 1, 1970.
Change opacity from 3 minute aggregate in 60 minutes to 6-minute averages
WOLF!