## Slide 1
Colored Art Glass Manufacturing Facility Temporary Rulemaking
EQC Proposed Rule Adoption
April 2016
Leah Feldon and George Davis| Oregon Department of Environmental Quality
Notes: (1 min.)
Good morning Chair O’Keeffe, Commissioners, my name is Leah Feldon and I manage the Office of Compliance and Enforcement. With me today is George Davis, engineer and senior permit writer for DEQ’s northwest region.
We are here today to present to you a proposal for temporary rules that would apply to colored art glass manufacturers in the Portland Air Quality Maintenance Area.
We proposed rules at the Commission’s meeting on March 15, which the Commission considered, but did not adopt. Instead the Commission granted a 14 day public comment period so that interested parties could comment on the rules being proposed. After the comment period, and consideration of the comments, we are here today to propose the temporary rules again, though they are different than the rules proposed in March, based on comments received.

## Slide 2
Summary of public comments
Addendum
Summary of proposed rule changes
Additional rule changes
Recommendations
Outline of Today’s Presentation
Notes: (1 min.)
Here is an outline of what we will discuss today, and we want to leave plenty of time for questions. Please fee free to ask questions throughout the presentation.
First we will discuss the nature and categorization of the public comments received;
Then we will discuss an addendum to the staff report for the proposed rules;
Next we will walk you through the proposed rule changes from the version proposed in March; and some additional changes that we would like to make to the current version; and
Finally, we will make our recommendation to you.

## Slide 3
Public Comment continued
523 Oregonians
671 worldwide
1194 Comments
Notes: (1 min.)
This is a high level depiction of the public comments.
Through the public comment process, we received comments from about 1200 individuals and organizations, 523 of those were from Oregonians and 671 were from parties outside of Oregon.
Some of the comments were from organizations representing the interests of their members. The total number of people represented by these comments is much greater than the number of comments we received. (3268 EPAC members)
The comments from parties outside of Oregon were almost exclusively from artists and customers who did not support regulation of colored art glass manufacturers.
As you can imagine, there are many perspectives expressed by those comments.

## Slide 4
Public Comment continued
Rule Support/Opposition* |  |  | 
Supports Temporary Rule | Supports Balanced Rule | Opposes Temporary Rule | Supports Statewide Rule
319 | 109 | 704 | 346
* Some commenters fall into multiple categories.
Notes: (1 min.)
This slide shows general support or opposition to the proposed rule. We just wanted you to see where the comments were in support or opposition to the proposed temporary rule and for statewide regulations.
The numbers here do not add up to the total number of comments received because some comments fell into more than one category. For example, some commenters support adoption of a temporary rule but also support a statewide rule. Likewise, some oppose a temporary rule but would also support adoption of industry wide statewide rules.
We consider all of the comments we receive, no matter how many people made the comment.

## Slide 5
Public Comment continued
 | 12 Categories | 92 Subcategories
1194 comments, organized into 12 categories and 92 subcategories | Health | 17
 | Emission Control Device/Testing | 15
 | General Rulemaking | 11
 | Metals | 11
 | Monitoring | 9
 | Permitting | 7
 | Colored Glass Manufacturing | 5
 | Timing | 3
 | Regional Issues | 3
 | Modeling | 2
 | Other Air Pollution Sources | 2
 | Other Comments | 7
Notes: (1 min.)
To review and respond effectively, we have organized the comments into the above 12 categories and further into 92 subcategories and that is also how we responded to them. Therefore you’ll see in your materials that we have 92 responses to comments.
We received a number of comments around many topics. Later in the presentation, George will discuss the changes we made based on the comments but first I want to also discuss a common theme we heard about adopting a human health and risk based approach to regulating industrial air toxics. Many of those comments identified that this temporary rulemaking will not address risk from other types of industries or in areas beyond Portland. We addressed those in the response to comments but wanted to reiterate here that the proposed rules are designed to address localized emissions solely from colored art glass manufacturers that was initially identified from ambient air monitoring. This temporary rule is not and never was designed to address any of these larger concerns. In order to do that, we need more time and a much larger stakeholder and public involvement process. Later in the agenda, you’ll hear more about DEQ’s plan moving forward to undertake a regulatory overhaul addressing air toxics from all industrial sources statewide.
In this temporary rule, we have included some elements of a human health and risk based program and are also using some elements of a technology based program. You’ll hear more about those as we go through some of the changes we made in response to comments.
Emission Control Device/Testing
General Rulemaking – why are you doing temp rule? Support/oppose temp rule, support statewide rule, use existing air toxics rules, do not listen to commenters that are out of state, DEQ caters to industry
Permitting – require permits, prohibit use of metals until permitted, lower threshold for permit, penalties, permits online
Timing – why 09/16, temp rule expiration before companies required to submit permit application
Regional Issues – create regional air pollution authority, use precautionary principle like City and Multnomah county, Cully neighborhood issues
Other Air Pollution Sources – mobile sources, previous industries at CAGMs
Other Comments – chromium in cement, long term impacts, expand affected parties, community right to know

## Slide 6
  Applicability of NESHAP
 | EPA Rule - Subpart SSSSSS | DEQ Temporary Rule
Applies to 6 metal HAPs | Yes | Yes
Affected furnace/facility | Each furnace that produces at least 50 tons per year of glass containing metal HAP as raw materials | Each facility that produces at least 10 tons per year of glass containing metal HAP as raw materials
Affected facilities in Oregon | 2 | 5
Chromium VI regulated | Not directly | Addressed directly
Technology or risk based | technology only | technology and risk
Notes: (3 mins.)
Before we get into those specific changes, I want to talk about the federal regulation for glass manufacturers.
We included an addendum to your staff report for this item which discusses the federal regulation and also DEQ’s finding of a continued need for this temporary rule.
The federal regulation that applies is referred to as the area source glass manufacturing NESHAP, short for National Emission Standard for Hazardous Air Pollutants.
On March, 9, DEQ requested clarification from EPA as to whether Bullseye and Uroboros have furnaces that EPA would consider to be “continuous” as defined in the NESHAP.
On April 12, EPA clarified that the furnaces at Bullseye and Uroboros meet the definition of “continuous furnace.” The following day, DEQ notified both companies that they are subject to the federal NESHAP.
Being subject to the NESHAP does not mean that every furnace at the facilities using metals must be controlled. This gets to why DEQ is still proposing the temporary rules despite its finding that the NESHAP applies.
DEQ included the addendum to the staff report justifying why these temporary rules are still necessary and why serious prejudice to the public interest would still occur despite the NESHAP applicability. The justification is three-fold:
  First, the federal NESHAP would require control devices for furnaces that produce 50 tpy of glass with metals or more. This would exclude the Tier 1 facilities that are included in the temporary rule.
  Second, even at the Tier 2 facilities, the NESHAP only requires controls on furnaces that produce 50 tpy of glass with metals, and both facilities have furnaces that produce less. The temporary rule would apply to these furnaces that produce less.
  Third, the NESHAP does not address emissions of hexavalent chromium. The temporary rule requires that Tier 2 CAGMs source test and model to determine maximum usage rates for trivalent chromium and also prohibits Tier 1 and Tier 2 facilities from using hexavalent chromium in any uncontrolled furnace.
For these reasons, DEQ finds that this temporary rule is necessary to prevent serious prejudice to the public interest. Now I’m going to hand it over to George to walk you through the changes …..

## Slide 7
Split CAGMs into two tiers
Tier 1 (smaller) | Tier 2 (larger)
No chromium VI in uncontrolled furnaces | No chromium VI in uncontrolled furnaces
Three options: Install emission control devices by 10/01/16 Demonstrate exemption is met Request permit prohibition on use of metals | Install emission control devices on all furnaces that use any of the 6 metals by 09/01/16
Test emission control device efficiency, if installed | Test emission control device efficiency
Test for metals if exemption is used | Test for chromium III to VI conversion
Modeling only required if exemption is used | Use dispersion modeling to determine chromium VI impact
Notes: (3 mins.)
Chair O’Keefe and Commissioners, DEQ made a number of changes to the proposed rule based on the comments we received. At this time I’d like to describe a few of the most significant changes for you.
One of the most significant changes we are proposing today is to split the colored art glass manufacturers into two tiers. Tier 2 includes the two larger manufacturers, Bullseye and Uroboros, and Tier 1 includes the three small manufacturers. This split was made because the smaller manufacturers produce much less glass than the larger facilities, and because there are some significant process differences.
Recall as Leah mentioned earlier, in this temporary rule, we have included some elements of a risk based program and are also using some elements of a technology based program.
The first requirement on the slide applies to both Tier 1 and Tier 2, and is prohibition on the use of chromium VI in uncontrolled furnaces.
The second requirement pertains to emission controls. The larger Tier 2 manufacturers must install emission controls on all furnaces that use any of the six regulated metals.
I’d like to note here that this is a technology based standard. We aren’t proposing that the emissions of most metals meet specific targets; instead we are simply requiring the installation of emission controls.
Regarding emission controls, the smaller Tier 1 manufacturers have three options: they can install emission controls; or they can demonstrate that they are exempt from having to install emission controls; or they can ask for a permit condition prohibiting the use of one or more of the metals.
The next requirement is to test their emission control device for efficiency. This is required of the Tier 2 manufacturers, but is only required of the Tier 1 manufacturers if they install emission controls.
The next requirements pertain to metals emissions testing and dispersion modeling. The larger Tier 2 manufacturers are required to test for total chromium and chromium VI and perform dispersion modeling to determine the impact of their emissions. The smaller Tier 1 manufacturers only have to test for metals and perform dispersion modeling if they want to use the exemption option.
These two elements of the proposed rules are risk-based instead of technology based. The goal of the emission testing and modeling is to show that the facility’s emissions do not result in ambient impacts that exceed specified risk-based concentrations.

## Slide 8
Expand list of regulated metals from three to six
Change definitions of CAGM, cullet and raw material for clarity
Clarify source test requirements
Proposed Rule Changes
Notes: (1 min.)
The rule proposed in March regulated only 3 metals; the rule proposed today regulates 6 metals (As, Cd, Cr, --- Pb, Mn, Ni)
To help clarify the applicability of the proposed rule, we revised the definitions of colored art glass manufacturer, cullet, and raw material.
We also simplified and clarified the source testing procedures for the larger, Tier 2 manufacturers

## Slide 9
Increase emission control device monitoring to:
  inlet temperature
  differential pressure
  periodic inspections
Remove emission control device particulate matter performance standard, retain 99% control efficiency
Proposed Rule Changes continued
Notes: (1 min.)
We revised the emission control device monitoring requirements. The rule proposed in March only addressed temperature as part of the design consideration. The rule proposed today also specifies inlet temperature monitoring, differential pressure monitoring and periodic inspections of the baghouse ducting, housing and interior.
For demonstrating emission control device efficiency, the rule proposed in March gave a choice of meeting a pounds of particulate matter per ton of glass standard, or a 99% control efficiency standard.
In reconsidering that choice we concluded that the pounds of particulate matter per ton of glass standard is not directly related to health risk, nor does it necessarily show the control device efficiency.
In today’s proposed rule, we have removed the pound per ton option and retained only the 99% control efficiency standard.

## Slide 10
Remove 1.6 ng/m3 total ambient concentration limit for chromium VI
  Replace with daily and annual acceptable source-only impact levels
Change ambient protective criteria
Notes: (3 mins.)
Another change we’ve proposed is to the ambient protective criteria.
The rule proposed in March included a total ambient concentration limit, that included background concentrations as well the source impact.
In reconsidering this standard, we identified three problems:
First, the idea was that the source’s impact, plus the background concentration from other sources, could not exceed the specified level. But this didn’t consider the possibility that the background concentration might exceed the specified level. This would imply that the facility couldn’t emit anything, which would put the entire burden on the facility when in fact other sources were causing the high levels.
Second, the original proposal was to allow the source to use up whatever difference there was between background and the specified level. It would be inappropriate to allow a single source to use up of the available margin.
And third, we realized that this approach was dependent on having ambient monitoring data for all sites. The reality is that we probably won’t have ambient monitoring data in most cases.
To address these problems, we are proposing instead to set maximum source impact levels, which are concentrations that the source’s emissions can result in, regardless of what the background concentration is. The proposed levels have been set at protective levels which are equal to the Ambient Benchmark Concentrations, except for lead, which is set at 1/10th of the ABC.

## Slide 11
Tier 2 CAGMs must model chromium VI impacts
  Cannot exceed acute or chronic impact limits
If Tier 1 CAGMs model for exemption, must model impacts of all metals used
  Cannot exceed chronic impact limit
  Because of model used, this is also protective of acute impact limits
Change ambient protective criteria
Notes: (3 mins.)
As mentioned earlier, the rules require some dispersion modeling to determine the impact of a facility’s emissions of certain metals.
For the larger Tier 2 facilities, the modeling requirement applies only to chromium VI impacts, with the objective of showing that the facility’s emissions of chromium VI will not cause an exceedance of either the acute or chronic impact levels specified in the rules.
The smaller Tier 1 facilities are only required to perform modeling if they choose the exemption option. In that case, they must model for all of the metals they want the exemption for, and must show that their impact does not exceed the specified chronic levels. We are also proposing that they use a different type of model that is much simpler and less expensive to use. This type of model gives a worst-case result so modeling for the chronic level is also protective of the acute level.

## Slide 12
OAR 340-244-9040(2) does not identify the metal that the text refers to. DEQ proposes to refer to chromium VI:
  “…annual acceptable source impact level of 0.08 nanograms per cubic meter of chromium VI and a daily acceptable source impact level of 36 nanograms per cubic meter of chromium VI.”
Changes in Proposed Rules - Addendum
Notes: (1 min.)
In addition to the changes just described, we are proposing two additional changes in an addendum to the staff report.
The first change is minor and simply involves correcting the rule text to specify the metal that part of the rule applies to.

## Slide 13
Chromium VI modeling at Tier 2 CAGMs must show:
Acute protective level applies anywhere off site (including streets and sidewalks – people present infrequently or for short periods)
Chronic protective level is not exceeded at nearest sensitive receptor (residence, hospital, school, daycare center - people present over long periods )
Changes in Proposed Rules - Addendum
Notes: (2 mins.)
The other change we’re proposing involves the receptor locations that must be used for the dispersion modeling.
When the Tier 2 manufacturers perform dispersion modeling, they have to meet both acute and chronic impact standards.
Acute impacts are impacts than could affect a person immediately, so this standard should apply anywhere a person might be for even a short period of time. This would include all locations off the facility’s site, including streets and sidewalks.
On the other hand, chronic impacts are impacts that may occur from long-term exposure, so the standards should apply to locations where people may be present for significant amounts of time, such as residences, schools and hospitals.
For these reasons we’re suggesting that the proposed rule be revised to specify these different receptor locations for acute and chronic modeling.
That ends my portion of the presentation and I’ll turn it back over to Leah.

## Slide 14: Recommendation
DEQ recommends that the Environmental Quality Commission:
approve and adopt the findings justifying adoption of a temporary rule as set forth in the staff report and the addendum to the staff report, and
that the Commission adopt the proposed temporary rules in attachment A, as amended by the addendum, as part of chapter 340 of the Oregon Administrative Rules.
Notes: (1 min.)