## Slide 1: Air Quality Program
Proposed Permanent
Colored Art Glass Manufacturing (CAGM) Rules
Sept. 29, 2016
Portland
Jaclyn Palermo and George Davis | Oregon Department of Environmental Quality
Notes: (1 min.)
Good morning Chair O’Keeffe, Commissioners, my name is Jaclyn Palermo and I manage the Air Quality Operations Section at the Department of Environmental Quality.
With me today is George Davis, engineer and senior permit writer for DEQ’s northwest region. David Farrer from Oregon Health Authority is also here and will be able to answer any toxicology related questions after the presentation. Feel free to ask clarifying questions during the presentation. We left room at the end of the presentation for the three of us to answer your questions.
We are here today to present to you a proposal for permanant rules that would apply to colored art glass manufacturers.
We proposed rules temporary glass rules at the Commission’s meeting on April 21 2016, which the Commission adopted. The temporary glass rules sunset on October 18, 2016. We are here today to present the proposed rules, which would replace the temporary rules and make the requirements permanent.

## Slide 2
Brief History/refresher
Summary of public comments
Summary of the changes from the temporary art glass rulemaking
Recommendations
Outline of Today’s Presentation
Notes: (1 min.)
Here is an outline of what we will discuss today.
First we will provide you with a brief refresher of the history of the temporary glass rulemaking.
Then we will discuss the comment process for this proposed rule as well as the nature and categorization of the public comments received;
Next we will walk you through the proposed rule and the changes from the temporary glass rulemaking adopted in April 2016; along with the rationale for making the changes.
Finally, we will make our recommendation to you.

## Slide 3
History
Glass facility
DEQ Monitor
Notes: (1 min.)
I give an abridged history of this proposed rule. George will then give the technical basis and rationale.
Elevated levels of hazardous air pollutants were found in the air around two glass manufacturing facilities in Portland. After a moss study and subsequent air monitoring in October 2015, DEQ confirmed that a glass company was the likely source. DEQ also identified a second area of concern near the glass company in North Portland.
The glass companies were operating in compliance with the current laws at the time. To address the gap and the elevated levels of hazardous air pollutants, DEQ proposed an art glass manufacturing temporary rulemaking, which was approved on April 21, 2016. If no action is taken the temporary rules will expire on Oct. 18, 2016. The proposed rule DEQ is presenting today would replace the temporary rules and make the requirements permanent.
The permanent rules that DEQ proposes for EQC adoption are intended to ensure that air emissions from colored art glass manufacturers do not cause unsafe levels of glassmaking hazardous air pollutants in the air nearby.
(arsenic, cadmium, chromium, lead, manganese, nickel and selenium)

## Slide 4
Public Comment
July 19, 2016 public hearing
Notes: (1 min.)
In addition to holding two fiscal committee meetings, DEQ held a public hearing on July 19, 2016 and accepted public comments from June 15, 2016 thru July 29, 2016.
DEQ’s public notice for this rulemaking included proposed rule language that was unchanged from the temporary rule, along with a request from DEQ for comments on several possible changes that were identified during the fiscal committee meetings. The three questions that were included in the public notice were:
Should the rule be modified to apply to sources that make less than 10 tons per year of colored art glass?
Should the rule be modified to apply statewide, rather than only in the Portland Air Quality Maintenance Area?
Should the control devise for incoming particulate matter standard be replaced with one based on the particulate matter at the outlet of the control device instead?

## Slide 5
Public Comment continued
41% From Oregon
47% elsewhere in the US
7% outside of the US
136 commenters, which includes businesses & organizations
Notes: This is a high level depiction of the public comments.
Through the public comment process, we received comments from about 136 individuals and organizations. DEQ received 151 comments from the 136 individuals. 41% of the commenters were from Oregon, 54% were from parties outside of Oregon, and 5% of the commenters did not state where they reside.
As you can imagine, there are many perspectives expressed by those comments.
I also want to not that we consider all of the comments we receive, no matter how many people made the comment.

## Slide 6
Public Comment continued
 | 10 Categories | 60 Subcategories
151 comments by 136 commenters, organized into 10 categories and 60 subcategories | Rule Applicability | 10
 | Enforcement | 2
 | General Rulemaking | 4
 | Health | 7
 | Other Pollution Sources | 2
 | Permitting | 2
 | Pollution Control Devices | 7
 | Public Outreach | 6
 | Rule Requirements | 14
 | Source Testing | 6
 | Total: | 60
 | Note: Some comments fall into multiple categories | 
Notes: (1 min.)
To review and respond effectively, we have organized the comments into the above 10 categories and further into 60 subcategories and that is also how we responded to them. Therefore you’ll see in your materials that we have 60 responses to comments.
We received a number of comments around many topics. Later in the presentation, George will discuss the changes we made from the temporary rule based on the comments.
This is a high level depiction of the public comments.
Through the public comment process, we received comments from about 136 individuals and organizations (with 151 comments), 41% of the commenters were from people of Oregon, 54% were from parties outside of Oregon, and 5% of the commenters did not state where they reside.
Some of the comments were from organizations representing the interests of their members. The total number of people represented by these comments is much greater than the number of comments we received.
As you can imagine, there are many perspectives expressed by those comments.
We addressed those in the response to comments but wanted to reiterate here that the proposed rules are designed to address emissions solely from colored art glass manufacturers. This glass manufacturing rule is not and never was designed to address any of these larger concerns. In order to do that, we established a much larger stakeholder and public involvement process and is being handled in a separate regulatory reform rulemaking, otherwise referred to as Cleaner Air Oregon.
In this proposed permanant rule, we have included some elements of a human health and risk based program and are also using some elements of a technology based program. You’ll hear more about those as we go through some of the changes we made in response to comments. You will now hear from George Davis. He will be discussing the changes and the associated rationale.

## Slide 7: Temporary rule requirements
Temporary Colored Art Glass Manufacturer (CAGM) rules
Intended to regulate emissions from:
  2 larger (Tier 2) CAGMs
  3 smaller (Tier 1) CAGMs
Rules only applied in Portland area
George Davis and Jaclyn Palermo | Oregon Department of Environmental Quality
Notes: The temporary colored art glass manufacturer rules were intended to regulate 5 colored art glass manufacturing facilities in the Portland area. The five facilities were split into two tiers based on how much glass they made and the type of glassmaking furnaces they used.

## Slide 8: Temporary rule requirements
Tier 1 (smaller) | Tier 2 (larger)
Three options: Install emission controls; or Test/model to show exempt; or Permit limit prohibiting use of one or more glassmaking HAPs | Install emission controls Limit chromium usage Test/model to establish chromium usage limits
Test emission control device to show 99.0 percent particulate matter (PM) control efficiency | 
George Davis and Jaclyn Palermo | Oregon Department of Environmental Quality
Notes: The rules imposed different requirements for the two tiers.
The smaller Tier 1 facilities were given three compliance options: install emission controls to control glassmaking hazardous air pollutant emissions; or do emissions testing and modeling to demonstrate that the ambient impacts of their emissions were below specified protective levels; or request permit prohibitions on the use of one or more of the glassmaking HAPs.
The larger Tier 2 facilities were required to install emission controls to control glassmaking HAP emissions, and the rules required that usage limits be established for the use of chromium. Associated with the chromium usage limitation was a requirement to perform emissions testing and modeling to determine the chromium usage limit.
Both Tiers were required to test their emission control devices and show that the emissions controls could meet a 99.0 % control efficiency.

## Slide 9
PROPOSED PERMANENT RULES | TEMPORARY RULES
(1) Apply at 5 tons per year or more of glass using glassmaking HAPs | 10 tons per year or more
(2) Apply statewide | Portland AQMA only
(3) & (5) Test to show 0.005 gr/dscf; Bag leak detection system; HEPA afterfilter | Test to show 99.0% particulate matter (PM) control efficiency
(4) Add Selenium to glassmaking HAPs | Arsenic, Cadmium, Chromium, Manganese, Nickel, Lead
(6) Set 24-hr health benchmark for Chromium +6 to 5 nanograms per cubic meter | 36 nanograms per cubic meter
(7) Test Chromium emissions at control device outlet (Tier 2) | Test Chromium at control device inlet; Calculate chromium out using PM control efficiency
(8) Compliance extensions to install emission controls; up to 1 year Tier 1 | No compliance extensions
Notes: This slide summarizes the most significant differences between the proposed permanent glassmaking rules and the temporary rules.
All of the changes that are proposed are based on comments that were received during the public comment period.
Eight changes are listed on pages 3 and 4 in the staff report, but the third and fifth listed changes are closely related so they’ve been combined on this slide. The numbers in the first column correspond to the list in the staff report.
I’ll quickly list the significant differences, and will then provide a little more information on each item in the following slides.
Change the rule applicability threshold from 10 tons per year of glass made using glassmaking HAPs to 5 tons per year.
Make the rules apply statewide instead of only in the Portland area.
(3) and (5) Replace the 99.0% particulate matter control efficiency test with three different options. Those options are: test to see that the control device meets 0.005 grains per dry standard cubic meter; or install a bag leak detection system; or install a HEPA afterfilter.
(4) Add selenium to the list of glassmaking HAPs regulated under this rule.
(6) Lower the 24-hour health benchmark for chromium +6 from 36 ng/m3 to 5 ng/m3.
(7) Test chromium emissions at the emission control device outlet instead of at the control device inlet.
(8) Provide compliance extensions for Tier 1 facilities of up to 1 year.
In addition to the more significant changes listed in this slide, a number of other changes were made, such as giving facilities outside the Portland area additional time to comply with the rules, to help clarify parts that some people found confusing, and for general housekeeping.

## Slide 10: (1) Apply at 5 tons per year or more of glass using glassmaking HAPs
Requested input in public notice
Many comments suggested lower threshold
DEQ agrees, but rules should not apply to individual artists/hobbyists
Some Tier 1 CAGMs in Portland AQMA
  Below threshold now
  Will likely exceed threshold as production increases
George Davis and Jaclyn Palermo | Oregon Department of Environmental Quality
Notes: Item 1, DEQ is proposing to lower the rule applicability threshold from 10 tons per year of glass made with glassmaking HAPs to 5.
Some commenters suggested making the rules apply if any amount of glass were made using HAPs, but DEQ does not believe the rules should apply to glass artists or hobbyists.
Staff propose 5 tons per year of glass as an appropriate balance between under- and over-regulating color art glass manufacturers.
Staff estimated that producing 5 tons of glass per year would require two small glass making furnaces, each making 50 pounds of glass two times per week.
DEQ considers this level of production to reasonably represent a level that defines a manufacturing operation, but is high enough to exclude artists and hobbyists who might make their own glass for special purposes.

## Slide 11: (2) Apply statewide
Requested input in public notice
Many comments suggest statewide applicability
LRAPA agrees
George Davis and Jaclyn Palermo | Oregon Department of Environmental Quality
Notes: Item 2, many comments suggested making the rules apply statewide.
Since the rules are intended to reduce the possible health threat from colored art glass manufacturers, DEQ agrees that the rules should apply statewide.
Staff have discussed the rules with the Lane Regional Air Pollution Authority, and they agree with making the rules apply statewide.

## Slide 12: (3) & (5) Test to show 0.005 gr/dscf; Bag leak detection system; HEPA afterfilter
Temporary rules: test emission control device
Show it meets 99.0 percent control efficiency for particulate matter
DEQ expected relatively simple, inexpensive testing
Test cost estimates far exceed DEQ’s expectations
George Davis and Jaclyn Palermo | Oregon Department of Environmental Quality
Notes: Items 3 and 5. The temporary rules required the affected glass manufacturers to test their emission control devices and show that they meet a 99.0% control efficiency for particulate matter. This is not a health-based standard, since DEQ has no information to correlate particulate matter emissions with glassmaking HAP emissions. The primary purpose of this testing was to ensure that the emission control system was working well.
Staff expected this testing to be relatively simple and inexpensive, but estimates for testing at some facilities are well over $100,000. This is because emissions will be so low that extraordinarily long test times will be required to collect enough of a sample to get a valid result.

## Slide 13: (3) & (5) Test to show 0.005 gr/dscf; Bag leak detection system; HEPA afterfilter
To indicate baghouse is working, 3 new options:
  Tier 1 – test for 0.005 grains/dry std. cubic foot OR
  install BLDS OR
  install HEPA afterfilter
  Tier 2 – test for 0.005 grains/dry std. cubic foot AND
  {install BLDS OR install HEPA afterfilter}
George Davis and Jaclyn Palermo | Oregon Department of Environmental Quality
Notes: Staff considered whether there are other ways to provide assurance that the emission control systems are working, and identified 3 options:
Test emissions and show that they do not exceed 0.005 grains per dry standard cubic foot of particulate matter. Oregon rules include a general particulate matter standard that ranges from 0.10 to 0.17 grains per dry std. cubic foot. The proposed level was suggested by EPA staff, and would be a good indicator that the emission control device is working well.
Another good indicator that a baghouse is working well is a bag leak detection system. These systems use a probe installed in the baghouse outlet that can detect increases in particulate matter emissions. Bag leak detection systems are very sensitive and can detect leakage in a baghouse that is too small to be detected by other means.
Finally, another option is to install a HEPA filter to further filter the baghouse exhaust. HEPA stands for High Efficiency Particulate Arrestance, and HEPA filters are so fine that they would plug up rapidly if used as the primary filtering medium. However, this tendency to plug up makes them work like a leak detection system. If the primary filter begins to leak, the HEPA filter will rapidly plug up, indicating that there is a leak. Further, the HEPA filter will continue to filter the emissions until the problem can be resolved.
DEQ is proposing that the smaller Tier 1 facilities have the option of testing for 0.005 gr/dscf, or installing a bag leak detection system, or install a HEPA afterfilter.
However, the larger Tier 2 facilities would be required to test for 0.005 gr/dscf, and would have the option of installing a bag leak detection system or a HEPA afterfilter.

## Slide 14: Bag Leak Detection System
George Davis and Jaclyn Palermo | Oregon Department of Environmental Quality
Notes: This is a general illustration of a baghouse, with dusty air entering at the inlet. The yellow are represents the filters, which filter the dusty air, and the filtered air then exists from the baghouse outlet.
A bag leak detection system probe is installed in the outlet duct and is connected to the electronic monitoring and recording system.

## Slide 15: HEPA Afterfilter
George Davis and Jaclyn Palermo | Oregon Department of Environmental Quality
Notes: This is a generalized illustration of a HEPA afterfilter. The afterfilter is installed in the baghouse outlet duct and provides additional filtering. If a leak develops in the baghouse, the HEPA filter will rapidly plug and cause a pressure increase that can be easily monitored.

## Slide 16: (4) Add Selenium to glassmaking HAPs
Original list of glassmaking HAPs: Arsenic, Cadmium, Chromium, Manganese, Nickel and Lead
Comments suggested adding more/all HAPs
High levels of Selenium monitored during the summer in SE Portland
Levels of other glassmaking HAPs low
George Davis and Jaclyn Palermo | Oregon Department of Environmental Quality
Notes: Getting back to the list of differences, item 4, commenters suggested that more HAPs should be regulated under this rule, some even suggesting that all HAPs should be regulated.
Staff do not recommend regulating all HAPs under this rule because the temporary rule was originally narrowly focused to solve a particular problem and staff recommend keeping these rules narrowly focused. In addition, DEQ is working to develop a broader Cleaner Air Oregon rules to regulate toxic air emissions from all industrial sources, which most likely will regulate a larger number of air toxics, and which may ultimately replace this rule altogether.
However, staff do recommend adding selenium to the list of glassmaking HAPs regulated under this rule because relatively high levels of selenium were monitored in SE Portland several times during the summer.
Phase in of selenium requires extending some compliance dates, since affected facilities have only learned about this change very recently.

## Slide 17: (6) Set 24-hour health benchmark for Chromium +6 to 5 nanograms per cubic meter
24-hr health benchmarks were established in addition to the annual Ambient Benchmark Concentrations
Are under review by OHA and DEQ at this time
OHA recommended lowering to 5 ng/m3
George Davis and Jaclyn Palermo | Oregon Department of Environmental Quality
Notes: Item 6, DEQ is proposing that the 24-hour health benchmark for chromium +6 be lowered from 36 ng/m3 to 5 ng/m3.
24-hour health benchmarks were established in the temporary rule, and were based on a survey of other states’ regulations.
The 24-hour health benchmarks are under review at this time, with chromium +6 being one of the first to be reviewed. Based on this review, OHA recommends lowering the level to 5 ng/m3 and DEQ agrees with this recommendation.

## Slide 18: (7) Test Chromium emissions at control device outlet (Tier 2)
Temporary rules required testing for chromium +6 at control device inlet
Use this result and PM control efficiency to calculate chromium +6 emissions (at control device outlet)
Testing indicates this is a poor assumption
DEQ recommends testing directly at outlet
George Davis and Jaclyn Palermo | Oregon Department of Environmental Quality
Notes: Item 7. When the temporary rules were first proposed, one of the major questions was how much chromium was emitted in the form of chromium +6.
To answer this question, testing for chromium +6 was required at the baghouse inlet. Testing at the inlet was specified to ensure that enough sample would be captured to ensure a valid test result.
At that time, it was assumed that the control efficiency for chromium would be the same as the control efficiency for particulate matter, so the PM control efficiency result could be used to calculate the chromium +6 emissions. However, testing done this summer does not support that assumption.
DEQ is therefore proposing that chromium be tested directly at the control device outlet using a simpler, less expensive test method.
However, this test method cannot differentiate between chromium +6 and other forms of chromium, so the proposed rule also specifies that if this test method is used, the facility must assume that 100% of the chromium is in the +6 form.
The facilities may use the more expensive chromium +6 test if they choose to, but they are not required to use it.

## Slide 19: (8) Compliance extensions to install emission controls; up to 1 year Tier 1
Rules that require install of emission control systems typically include a provision
George Davis and Jaclyn Palermo | Oregon Department of Environmental Quality
Notes: And finally, item 8. Rules that require installation of emission control systems typically include a provision for facilities to request compliance extensions if installation is delayed for reasons beyond their control.
This can occur, for example, because of a strike at the control system manufacturer’s facility, or if delivery is delayed because of bad weather, or for a number of other reasons.
Without a provision for granting compliance extensions, facilities could find themselves in violation of the rules despite making a good faith effort to comply.
DEQ therefore recommends including a provision for granting compliance extensions of up to 1 year for reasons beyond the facilities’ control.

## Slide 20: End of rules presentation
Questions?
George Davis and Jaclyn Palermo | Oregon Department of Environmental Quality
Notes: This concludes my part of the presentation.

## Slide 21: Recommendation
DEQ recommends that the Environmental Quality Commission:
approve and adopt the findings justifying adoption of a permanant rule as set forth in the staff report.
George Davis and Jaclyn Palermo | Oregon Department of Environmental Quality
Notes: (1 min.)