## Slide 1: Oregon Clean Fuels Program
CFP 2018 Rulemaking
June 18 Advisory Committee Meeting
Oregon Department of Environmental Quality

## Slide 2: Meeting Agenda
Overview of rulemaking, current timeline
Updates to and results from the Greenhouse Gases, Regulated Emissions, and Energy Use in Transportation (GREET) and Oil Production Greenhouse gas Emissions Estimator (OPGEE) models
Updates to CFP standards, lookup table, substitute FPCs
Other housekeeping updates and enforcement rule changes

## Slide 3: Rulemaking Timeline
Meeting #4 – July 16th, 2018
  Draft regulatory text and fiscal analysis
Notice of Proposed Rulemaking – August 2018
EQC Meeting – November 2018
Meeting #1 for CFP 2019 rulemaking – December/January

## Slide 4: OPGEE analysis
The goal of this analysis was to update the baseline CI for crude oils used to produce the gasoline and diesel supplied to Oregon in 2015
CFP initially used the analysis performed by Lifecycle Associates in 2014 for Washington Office of Financial Management using 2012 data
DEQ does not plan to revisit this analysis for the 2015 baseline in future 3-year CI reviews unless significant new data or errors come to light

## Slide 5: OPGEE analysis
Use values from OPGEE 2.0’s results as of the 15-day package
Based on a review of available data, DEQ decided to analyze and use Washington state refineries’ crude slate to calculate the OPGEE value for all gasoline and diesel used in Oregon.
  Majority of gasoline and diesel comes from the Puget Sound Refineries
  Limited data on intra-US refined product movements
  Only public source of Utah refineries’ crude slates is missing >40% of the crudes being input into those refineries

## Slide 6: OPGEE analysis
Analysis relied on synthesizing two publicly-available datasets for 2015 crude oil inputs into Washington Refineries
  Washington Research Council report
  EIA Company Level Imports Data
Washington Research Council | 
Table A.3 | kbbl/Day
Alaska | 201
Conventional Canadian | 126.4
Oil Sands Canadian | 61.4
Bakken | 141
All Others | 35.7
EIA Company level imports | 
 | kbbl
Argentina | 2,696
Brazil | 1,062
Canada | 68,811
Ecuador | 745
Russia | 162
Saudi Arabia | 3,508

## Slide 7: OPGEE analysis
Given lack of crude field names, created jurisdictional average CI based on a straight average of all fields in OPGEE, other than Canada where Conventional and Oil Sands averages were created
 | kbbls/yr | 2015 CI Avg
Alaska | 73,365 | 15.91
Conventional Canadian | 46,136 | 8.40
Oil Sands Canadian | 22,411 | 23.88
Bakken | 51,465 | 9.73
All Others | 13,031 | 
Known All Others from EIA | 8,173 | 9.00
Remaining Unknown (~2%) | 4,858 | 
Known WA VWA CI |  | 13.22

## Slide 8: GREET 3.0
DEQ plans to adopt lightly regionalized version of CA-GREET 3.0 and the simplified calculators
  Oregon grid mix
  Other
To maintain compatibility between CA- and OR-GREET, DEQ does not plan to change other aspects of the model or calculators

## Slide 9: GREET 3.0
The simplified calculators cover:
  Starch and corn fiber ethanol
  Sugarcane ethanol
  Biodiesel and Renewable Diesel
  LNG and L-CNG
  Biomethane from landfills
  Biomethane from wastewater
  Biomethane from food, green, and other organic waste
  Biomethane from dairy and swine manure

## Slide 10: Lookup Table Changes
 | Existing CI | New CI
CBOB / Clear Gasoline | 100.77 | 100.39
ULSD / Clear Diesel | 101.65 | 102.07
Imported E10 | 98.64 | 98.29
Imported B5 | 99.61 | 100.01
Imported B20 | 93.41 | 93.75
Fossil CNG | 79.93 | 80.44
Fossil LNG | 94.46 | 86.97
Fossil LPG/Propane | 83.05 | 83.52

## Slide 11: Modified targets
 | Reduction percentage | Existing Gasoline Standard | Revised Gasoline Standard | Change | Existing Diesel Standard | Revised Diesel Standard | Change
2019 | 1.5% | 97.16 | 96.82 | -0.35 | 98.12 | 98.51 | 0.39
2020 | 2.5% | 96.18 | 95.83 | -0.34 | 97.12 | 97.51 | 0.39
2021 | 3.5% | 95.19 | 94.85 | -0.34 | 96.12 | 96.51 | 0.39
2022 | 5.0% | 93.71 | 93.38 | -0.34 | 94.63 | 95.01 | 0.38
2023 | 6.5% | 92.23 | 91.90 | -0.33 | 93.14 | 93.51 | 0.37
2024 | 8.0% | 90.75 | 90.43 | -0.33 | 91.64 | 92.01 | 0.37
2025 and beyond | 10.0% | 88.78 | 88.46 | -0.32 | 89.65 | 90.01 | 0.36

## Slide 12: New or updated EERs
Fuel Application | Existing EER | New EER
Alternative Jet | N/A | 1
On-Road Electric Motorcycle | N/A | 4.4
Electric Forklift | N/A | 3.8
Hydrogen Fuel Cell Forklift | N/A | 2.1
Propane Forklift | N/A | 1
Electric Transit Bus | 4.2 | 5
Electric Heavy Duty BEV or PHEV | 2.7 | 5
Aerial Tram | 2.5 | 2.6

## Slide 13: New or Updated EERs
EERs would take effect for 2019 and onwards
Electric Motorcycles will be inserted into the current structure for electric cars and be eligible for public and residential charging credits
Aerial Tram EER update was promised in last rulemaking as only 2 years of data were available at the time

## Slide 14: Substitute Fuel Pathway Codes
Substitute Fuel Pathway Codes (FPCs) are used when biofuels are transferred within the state without the carbon intensity information being passed along by the seller
They are set with conservatively low CIs to maintain the environmental integrity of the program
Currently, many reporting parties are attempting to use the Imported E10/B5 FPCs when reporting in-state transfers of products blended in-state where they do not wish to specify the FPC of the biofuel component of the blend

## Slide 15: Substitute Fuel Pathway Codes
Imported E10/B5/B20 FPCs were set with conservatively high CIs as the biofuel component was unknown
Substitute FPCs are used after the biofuel’s real FPC has been reported into the CFP Online System
Gap between the high CIs assumed for the imported FPCs (69.89 for Ethanol, 58.28 for Biodiesel) and the actual CI of delivered biofuels is increasing

## Slide 16: Substitute Fuel Pathway Codes
DEQ is proposing to create Substitute FPCs for blended fuels that should be used for purchases without obligation from a seller at a rack
Would create the fuel pathway codes for reporting for Q3 2018 and beyond
Rule change would require their use for in-state rack purchases except in cases where the rack seller specifies the biofuel CI
Substitute FPCs | 
E10 | 96.23
B5 | 97.97
B20 | 85.53

## Slide 17: Additional Credit Generation
Forklifts
  Allowing credit generation for electricity, hydrogen, and LPG
  Forklift fleet owner is eligible to generate credits
  Owner may designate an aggregator
  Credit generation as in the California LCFS
  Gasoline, diesel used in these applications is an obligated fuel
Truck refrigeration units
  Allow credit generation for electric TRUs
  Owner of the eTRU is eligible to generate credits
  Owner may designate an aggregator
  Diesel used in TRUs is an obligated fuel

## Slide 18: Alternative Jet
DEQ is considering allowing credit generation from alternative jet fueled into planes in Oregon
Alternative jet is generally coproduced with renewable diesel, addition of alternative jet intended to incent increasing production and supply of both fuels
DEQ would not create a compliance obligation for fossil jet fuel

## Slide 19: Alternative Jet
DEQ would mirror the California provisions on alternative jet
Credit generation will be measured against fossil jet CI until the Diesel pool targets intersect in 2025, at which point it will be measured against the Diesel pool target

## Slide 20: Comments & Next Steps
Comments due Tuesday, July 10th
  Email them to OregonCleanFuels@deq.state.or.us
  We say this every time, but you do not need to wait until the deadline to file comments
Next meeting is Monday, July 16th
  Back at the Portland State Office building
  Will make an effort to have documents posted the Friday before